## Slide 1: Autopilot
Team (4)

## Slide 2
Team members
name | sec | bn
Mohammed Ahmed Hassan Ahmed | 2 | 37
Ibrahim Thabet Allam | 1 | 1
Mohammed Hatem Mohammed Saeed | 2 | 39
Mohamed Hassan Gad Ali | 2 | 41
Mohammed Abd El Mawgoud Ghoneam | 2 | 43

## Slide 3: Autopilot literature review
Task 1

## Slide 4: Research questions
Autopilot
An autopilot is a system that allows an airplane to navigate without the need for constant manual control by a human operator

## Slide 5: Inputs and outputs of Autopilot system
inputs
  Control Inputs:
  Radio Control Receivers
  MAVLink Data Streams, ie ground control stations or companion computers
  Sensor inputs:
  GPS, Compass, Airspeed, Rangefinders, IMU
  Power Management Unit Inputs:
  Received Signal Strength Input (RSSI)
  Analog Airspeed Sensors

## Slide 6: Inputs and outputs of Autopilot system
Outputs
  ESCs (electronic circuit that controls and regulates the speed of an electric motor) for motors
  Servos for control surfaces
  Telemetry data
  Actuators and General Purpose I/O like LEDs, buzzers etc

## Slide 7: the role of the pilot in an airplane equipped with an autopilot
The pilot sets the flight plan and turn on the autopilot sometimes the pilot reprograms the autopilot in case if worked incorrectly. autopilot is not smart enough to fly a plane by It self

## Slide 8: What is the difference between Autopilot & SAS?
SAS (Stability augmentation system) generally used during low and slow maneuvering where the pilot may be making constant attitude changes in preparation for landing.
Autopilot do same functions as SAS in addition it provides more functions ,Autopilot Is more sophisticated than SAS

## Slide 9: Role of onboard sensors
Sensors provide the autopilot computers with data like speed, coordinates, position so the computers can estimate the states and give the correct control actions to the actuators for example
Gyroscope an IMU supplies the autopilot with position data so if the airplane in incorrect position it gives the actuator signal so that it can adjust position

## Slide 10: Flight Mechanics review
Assume
The body is rigid which means the mass is constant and there is no change in geometry (Stress calculations are neglected).
Fix a body axes at the center of mass of the rigid body.

## Slide 11: Flight Mechanics review
RBD
  calculations of linear momentum:
Get

## Slide 12: Flight Mechanics review
RBD
  calculations of angular momentum:
Get

## Slide 13: Flight Mechanics review
Now we are dealing with an aircraft which means that

## Slide 14: Flight Mechanics review
earth axis to body axis transformation:

## Slide 15: Flight Mechanics review
earth axis to body axis transformation:

## Slide 16: Flight Mechanics review
earth axis to body axis transformation:

## Slide 17: Flight Mechanics review
Let’s apply the above transformation on the gravitational force of the airplane as following:

## Slide 18: Flight Mechanics review
Then:

## Slide 19: Flight Mechanics review
Also we can get

## Slide 20: Flight Mechanics review
Classification of equations
  Kinetics equations

## Slide 21: Flight Mechanics review
Classification of equations
  Kinematics equations:

## Slide 22: Flight Mechanics review
The additional EOM of airplanes:
The effect of the control surfaces: , , ,
i- The change in forces:

## Slide 23: Flight Mechanics review
ii- The change in moments:

## Slide 24: Flight Mechanics review
The EOM’s are coupled, nonlinear and first order DE.
Difference bet. Body & inertial Axes
  Body axes: they are a set of axes which are fixed at the body in its translational and rotations.
  Inertial axes: they are a set of axes which are fixed at a specified position on the ground.

## Slide 25: Flight Mechanics review
Pitch angle: it’s the angle between the body y-axis and the horizon.
AOA: the angle at which the chord of an aircraft's wing meets the relative wind.
Sideslip angle: it’s formed due to lateral deviation between the plane and the direction of the flow.
Yaw angle (heading): it’s formed due to the rotation about z-axis.

## Slide 26: numerical solving algorithms for ODE
One-step methods, like:
Euler-Cauchy method
Improved Euler method
Raunge-Kutta method
Backward Euler method
Multistep methods, like:
Adams-Bash forth method
Adams-Moulton method
Other methods
Predector –coeector methods
Exponential integrator methods

## Slide 27: The chosen method for solving the aircraft EOM
We choose to use Raunge-Kutta method since its one of the most accurate one step methods used in the numerical solutions, in addition it’s the method used in the MATLAB ODE45 algorithm.
4th order Runge-Kutta

## Slide 28: Numerical Solver for the RBD Equations
Task 2

## Slide 29: Inputs
Initial Conditions
[𝒖_𝟎 𝒗_𝟎 𝒘_𝟎, 𝒑_𝟎 𝒒_𝟎 𝒓_𝟎, 𝝓_𝟎 𝜽_𝟎 𝝍_𝟎, 𝒙_𝟎 𝒚_𝟎 𝒛_𝟎 ]
Mass & Inertia
Forces
Moments
𝑰= [■8(𝑰_𝒙&𝑰_𝒙𝒚&𝑰_𝒙𝒛@𝑰_𝒚𝒙&𝑰_𝒚&𝑰_𝒚𝒛@𝑰_𝒛𝒙&𝑰_𝒛𝒚&𝑰_𝒛 )]=[■8(1&−2&−1@−2&5&−3@−1&−3&0.)]
Mass = 15 kg
F = [10 5 9]
M = [10 20 5]
Initial Conditions
Mass & Inertia
Forces
Moments
F = [10 5 9]
M = [10 20 5]

## Slide 30: System of Equations
Kinetics Equations
Kinematics Equations
{(█(𝜙@(█(𝜃@𝜓 ̇ )) ̇ )) ̇ }= [■8(1@0@0) ■8(𝑆𝜑 𝑇𝜃@𝐶𝜑@𝑆𝜑⁄𝐶𝜃) ■8(𝐶𝜑 𝑇𝜃@−𝑆𝜑@𝐶𝜑⁄𝐶𝜃)]{█(𝑃@𝑄@𝑅)}
𝐹_𝑥=𝑚(𝑢 ̇+𝑞𝑤−𝑟𝑣)
𝐹_𝑦=𝑚(𝑣 ̇+𝑟𝑢−𝑝𝑤)
𝐹_𝑧=𝑚(𝑤 ̇+𝑝𝑣−𝑞𝑢)
𝐿= (𝐻_𝑥 ) ̇+〖𝑞𝐻〗_𝑧−𝑟𝐻_𝑦
𝑀= (𝐻_𝑦 ) ̇+〖𝑟𝐻〗_𝑥−𝑝𝐻_𝑧
𝑁=(𝐻_𝑧 ) ̇+𝑝𝐻_𝑦−𝑞𝐻_𝑥
{(█(𝑋@(█(𝑌@𝑍 ̇ )) ̇ )) ̇ }= [■8(𝐶_𝜃 𝐶_𝜓&𝑆_𝜙 𝑆_𝜃 𝐶_𝜓−𝐶_𝜙 𝑆_𝜓&𝐶_𝜙 𝑆_𝜃 𝐶_𝜓+𝑆_𝜙 𝑆_𝜓 @𝐶_𝜃 𝑆_𝜓&𝑆_𝜙 𝑆_𝜃 𝑆_𝜓+𝐶_𝜙 𝐶_𝜓&𝐶_𝜙 𝑆_𝜃 𝑆_𝜓−𝑆_𝜙 𝐶_𝜓@−𝑆_𝜃&𝑆_𝜃 𝐶_𝜃&𝐶_𝜙 𝐶_𝜃 )]{█(𝑢@𝑣@𝑤)}
Kinetics Equations
Kinematics Equations

## Slide 31: Outputs
States
[𝒖 𝒗 𝒘, 𝒑 𝒒 𝒓, 𝝓 𝜽 𝝍, 𝒙 𝒚 𝒛]
(states values over the specified time span )
States

## Slide 32: Code Strategy
6DOF
Initial Conditions
Forces
RBD Solver
Moments
Inertia & Mass
Solving
Solving state by state using RBD Solver
Appling RK4 in order to evaluate the next state.
Evaluation of 12 equation for given set of inputs
Verifying
Using Simulink (equations)
Using ode45 (integration)

## Slide 33: Simulink

## Slide 34: Results & Verifying

## Slide 35: Results & Verifying

## Slide 36: Results & Verifying

## Slide 37: Results & Verifying

## Slide 38: Airplane Simulator Part II
Task 3

## Slide 39: Nonlinear model
Airframe
RBD
States
Gravity forces

## Slide 40: Forces Acting on A\C
Thrust
Aerodynamic forces
Gravity force

## Slide 41: Airframe equations
)
)
)
)
)
)
+

## Slide 42: The conditions on body axis
The center of the axis coincide on the CG of the body.
X-Z plane is the plan of symmetry.

## Slide 43: Types of body axis
Stability axis (x-axis coincide on the ).
Principle axis ().
Body axis (x-axis coincide on the FRL).

## Slide 44: Consequences of the linearization
For the linearization to be valid with an acceptable error the perturbations must be small.
Hance we usually choose one of the equilibrium points to linearize the equations around it; Using the steady state values at the given operating condition as a reference.

## Slide 45: steady level flight
there is no moments acting on the aircraft.
The forces acting on the aircraft must be in equilibrium.
The rate of change of states is zero.
Forces and moments in the body axis

## Slide 46: steady level flight
Whereexpress the aerodynamic forces.
And the total force acting on the airplane Equals the vectorial sum of the aerodynamic and gravity forces.

## Slide 47: Airplane Equations of Motion Linearization
Task 4

## Slide 48: Linearization
By using small perturbation theory we can linearize EOM’s of the airplane

## Slide 49: Reference Flight condition

## Slide 50: Linearization Technique
Step 1
step4
step3
Recast each variable in terms of a steady-state value and a perturbed value.
step2
Apply the small-angle assumption to trig functions of perturbed angle
Assume products of small perturbations are negligible.
Remove the steady-state equation from the perturbed equation.

## Slide 51: Notes in Lateral calculations

## Slide 53: State space Model:
Lateral

## Slide 54: short period & Long period approximations of the Longitudinal dynamics
By solving the A matrix we get 2 pairs of conjugate roots the pair which has small real part has big settling time according to on the other hand with the pair which has bigger real part
By solving the A matrix we get 2 pairs of conjugate roots the pair which has small real part has big settling time according to 𝑇_𝑠=4/(𝜁𝜔_𝑛 ) on the other hand with the pair which has bigger real part

## Slide 55: short period & Long period

## Slide 56: short period & Long period approximations of the Longitudinal dynamics
Short Period
Long period

## Slide 57: short period & Long period approximations of the Longitudinal dynamics
Short period Approx.
Long period Approx.

## Slide 58: Results due to elevator input 5 degree

## Slide 59: Results due to elevator input

## Slide 60: Results due to Thrust input 10000

## Slide 61: Results due to Thrust input 10000

## Slide 62
Auto Pilot
Task 5

## Slide 63
B.N. | Sec | Name
37 | 2 | Mohammed Ahmed Hassan Ahmed
1 | 1 | Ibrahim Thabet Allam
39 | 2 | Mohammed Hatem Mohammed Saeed
41 | 2 | Mohamed Hassan Gad Ali
43 | 2 | Mohammed Abd El MawgoudGhoneam
Team 4

## Slide 64
Introduction:
In order to Design a controller first of all we should get the transfer functions of all full longitudinal dynamics model.
Our methodology is to using inner loops architecture.
Then using SISO tool to design the controller.
Finally we use SIMULINK to check the performance of our design.

## Slide 65
Design Pitch Controller With Pitch Rate Feedback
servo

## Slide 66
Design Pitch Controller With Pitch Rate Feedback

## Slide 67
Design Pitch Controller With Pitch Rate Feedback
The open loop transfer function is:

## Slide 68: SISO Tool Design
Root locus

## Slide 69: SISO Tool Design
Root locus

## Slide 70: Step response
Control action
System Response

## Slide 71: Simulink test

## Slide 72: Simulink test

## Slide 73: Necessity of velocity control

## Slide 74: Necessity of velocity control
when we input positive pitch angle, the action depends on the thrust if the thrust is big enough to climb upward the airplane will climb upward if the thrust is not enough the airplane would dive downward but logically, when the pilot input a positive pitch the airplane should climb upward

## Slide 75: Necessity of velocity control

## Slide 76: Necessity of velocity control
Our plane climbs upward because it has enough thrust to accomplish this. But this not meaning that we control altitude because the airplane will climb to specific height that its thrust enough to reach, then the airplane would dive downward. And this specific height may be before or after that height we need to reach, so we need to control the velocity to reach to required altitude by change thrust ()

## Slide 77: NT-33A engine
Our aircraft ‘NT-33A’ was a training aircraft that was developed from the Lockheed martin.
The Powerplant installed is 1 × Allison J33-A-35 centrifugal flow turbojet engine, with 5,400 lbf (24 kN) thrust for take-off with water injection
4,600 lbf (20,461.82 N) maximum continuous thrust.

## Slide 78: Velocity Controller

## Slide 79: Velocity Controller

## Slide 80: Velocity Controller

## Slide 81: Step response & Control action
Step response
Control action

## Slide 82: Altitude controller

## Slide 83: Altitude controller

## Slide 84: Altitude Controller

## Slide 85: Step response & Control action
Step response
Control action

## Slide 86
simulation
Results

## Slide 87: Simulation Blocks

## Slide 88: Simulation Blocks

## Slide 89: Simulink Results of 1000ft Command

## Slide 90: Simulink Results of 1000ft Command

## Slide 91: Simulink Results of 1000ft Command

## Slide 92
Auto Pilot
Task 6

## Slide 93: Lateral Control
The rule of the lateral autopilot is to control the motion of the airplane in the lateral-directional plane, it controls the rudder & aileron to achieve a coordinated turn
What is coordinated turn ??

## Slide 94: coordinated turn We may call it “zero-lateral acceleration turn”
Normal flight
Medium banked turn
Steep banked turn
In terms of mechanics

## Slide 95: coordinated turn
When lift increases in one of the wings the drag also increases
On that wing resulting in “adverse yaw phenomenon”
To overcome this phenomenon we need rudder input
In terms of aerodynamics

## Slide 96: coordinated turn
The coordinated turn is a maneuver in which the airplane’s heading angle is changed (airplane turns) without “slipping or skidding”, i.e. the side slip angle (β = 0). note: skidding is having +ve sideslip angle (β>0) while slipping is having -ve sideslip angel (β<0)
In terms of aerodynamics

## Slide 97: “Yaw damper” for the Dutch roll mode
Design

## Slide 98: “Yaw damper” for the Dutch roll mode
Design

## Slide 101
Test The “Yaw damper” controllers on the full state space model

## Slide 102: Simulink Test

## Slide 103: Test Result

## Slide 104: Roll Controller

## Slide 105: Roll Controller
Design

## Slide 106: Response

## Slide 107: Control Action

## Slide 108: Coordination

## Slide 109: Lateral controller Test with Simulink

## Slide 110: Result

## Slide 111
Autopilot
Task 7

## Slide 112: Autopilot Testing on Non-Linear Simulation
Lateral Autopilot
Longitudinal
Autopilot
Autopilot Controller

## Slide 113: Autopilot Testing on Non-Linear Simulation
This task is depending on the comparison between lineal and non-linear simulators for the two portions of autopilot controller.
The comparison is mainly depending on the changes in the control surfaces: , ,

## Slide 114: Develop the testing loop containing the “Controller + Simulator”

## Slide 115: Develop the testing loop containing the “Controller + Simulator”

## Slide 116: Comparison bet. Linear & Nonlinear simulator in pitch controller

## Slide 117: Test the “Pitch controller” for
1- u

## Slide 118: Test the “Pitch controller” for
2-

## Slide 119: Test the “Pitch controller” for
3-

## Slide 120: Test the “Pitch controller” for
4-

## Slide 121: Test the “Pitch controller” for
5- h

## Slide 122: Test the “Pitch controller + Velocity controller” for 15
1- u

## Slide 123: Test the “Pitch controller + Velocity controller” for 15
2- Theta

## Slide 124: Test the “Pitch controller + Velocity controller” for 15
3- h

## Slide 125: Test the “Pitch controller + Velocity controller” for 15
4-

## Slide 126: Test the “Pitch controller + Velocity controller” for 15
5-

## Slide 127: Test the “Pitch controller + Velocity controller” for 15
6-

## Slide 128: Test the “Altitude Hold” of 1000 ft
1-

## Slide 129: Test the “Altitude Hold” of 1000 ft
2- u

## Slide 130: Test the “Altitude Hold” of 1000 ft
3-

## Slide 131: Test the “Altitude Hold” of 1000 ft
4- h

## Slide 132: Test the “Altitude Hold” of 1000 ft
5-

## Slide 133: Test the “Altitude Hold” of 1000 ft
6-

## Slide 134: Test the “Lateral controller” and compare the response with the same test on the State space model

## Slide 135: Test the “Lateral controller” and compare the response with the same test on the State space model

## Slide 136: Test the “Lateral controller” and compare the response with the same test on the State space model

## Slide 137: Test the “Lateral controller” and compare the response with the same test on the State space model

## Slide 138: Test the “Lateral controller” and compare the response with the same test on the State space model

## Slide 139: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 140: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 141: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 142: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 143: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 144: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 145: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 146: Test the “Lateral controller + Altitude Hold controller” and compare the response with the same test on the State space model

## Slide 147: Perform a complete autonomous mission including “climb, cruise, turn, descent”
6-

## Slide 148: Perform a complete autonomous mission including “climb, cruise, turn, descent”
6-

## Slide 149: Perform a complete autonomous mission including “climb, cruise, turn, descent”
6-

## Slide 150: Perform a complete autonomous mission including “climb, cruise, turn, descent”
6-

## Slide 151: Perform a complete autonomous mission including “climb, cruise, turn, descent”
6-

## Slide 152
Thanks