## Slide 1: Task 1 Autopilot literature review
Team members
name | sec | bn
Mohammed Ahmed Hassan Ahmed | 2 | 37
Ibrahim Thabet Allam | 1 | 1
Mohammed Hatem Mohammed Saeed | 2 | 39
Mohamed Hassan Gad Ali | 2 | 41
Mohammed Abd El Mawgoud Ghoneam | 2 | 43

## Slide 2: Research questions
Autopilot
An autopilot is a system that allows an airplane to navigate without the need for constant manual control by a human operator

## Slide 3: Inputs and outputs of Autopilot system
inputs
  Control Inputs:
  Radio Control Receivers
  MAVLink Data Streams, ie ground control stations or companion computers
  Sensor inputs:
  GPS, Compass, Airspeed, Rangefinders, IMU
  Power Management Unit Inputs:
  Received Signal Strength Input (RSSI)
  Analog Airspeed Sensors

## Slide 4: Inputs and outputs of Autopilot system
Outputs
  ESCs (electronic circuit that controls and regulates the speed of an electric motor) for motors
  Servos for control surfaces
  Telemetry data
  Actuators and General Purpose I/O like LEDs, buzzers etc

## Slide 5: the role of the pilot in an airplane equipped with an autopilot
The pilot sets the flight plan and turn on the autopilot sometimes the pilot reprograms the autopilot in case if worked incorrectly. autopilot is not smart enough to fly a plane by It self

## Slide 6: What is the difference between Autopilot & SAS?
SAS (Stability augmentation system) generally used during low and slow maneuvering where the pilot may be making constant attitude changes in preparation for landing.
Autopilot do same functions as SAS in addition it provides more functions ,Autopilot Is more sophisticated than SAS

## Slide 7: Role of onboard sensors
Sensors provide the autopilot computers with data like speed, coordinates, position so the computers can estimate the states and give the correct control actions to the actuators for example
Gyroscope an IMU supplies the autopilot with position data so if the airplane in incorrect position it gives the actuator signal so that it can adjust position

## Slide 8: Flight Mechanics review
Assume
The body is rigid which means the mass is constant and there is no change in geometry (Stress calculations are neglected).
Fix a body axes at the center of mass of the rigid body.

## Slide 9: Flight Mechanics review
Kinetics equations
Kinematics equations:

## Slide 10: Flight Mechanics review
Now we are dealing with an aircraft which means that

## Slide 11: Flight Mechanics review
earth axis to body axis transformation:

## Slide 12: Flight Mechanics review
earth axis to body axis transformation:

## Slide 13: Flight Mechanics review
earth axis to body axis transformation:

## Slide 14: Flight Mechanics review
Let’s apply the above transformation on the gravitational force of the airplane as following:

## Slide 15: Flight Mechanics review
Then:

## Slide 16: Flight Mechanics review

## Slide 17: Flight Mechanics review
The EOM’s are coupled, nonlinear and first order DE.
Difference bet. Body & inertial Axes
  Body axes: they are a set of axes which are fixed at the body in its translational and rotations.
  Inertial axes: they are a set of axes which are fixed at a specified position on the ground.

## Slide 18: Flight Mechanics review
Pitch angle: it’s formed due to rotation about y-axis.
AOA: it’s formed due to due to a difference between the direction of flow and the plane wing.
Sideslip angle: it’s formed due to due to lateral deviation between the plane and the direction of the flow.
Yaw angle (heading): it’s formed due to due to the rotation about z-axis.

## Slide 19: numerical solving algorithms for ODE
One-step methods, like:
Euler-Cauchy method
Improved Euler method
Raunge-Kutta method
Backward Euler method
Multistep methods, like:
Adams-Bash forth method
Adams-Moulton method
Other methods
Predector –coeector methods
Exponential integrator methods

## Slide 20: The chosen method for solving the aircraft EOM
We choose to use Raunge-Kutta method since its one of the most accurate one step methods used in the numerical solutions, in addition it’s the method used in the MATLAB ODE45 algorithm.
4th order Runge-Kutta

## Slide 21: Numerical Solver for the RBD Equations
Task 2

## Slide 22
6DOF
Initial Conditions
Forces
Runge-Kutta4
Evaluation of 12 equation for given set of inputs
RBD Solver
Appling RK4 in order to evaluate the next state.
Moments
Inertia & Mass
Solving
Solving state by state using RBD Solver